## Slide 1: Project Competition
Advisor: 葉廷仁 教授
TAs: 董祐華 林容緣 張弘豫 陳仕昕
Date: 2024/05/22

## Slide 2: Outline
Schedule
Simulation Contest
Real Arm Contest
Appendix

## Slide 3: 1. Schedule
期末考週
Simulation
Competition
In R402
Real Arm
Competition
In R402

## Slide 4: 2. Simulation Contest
競賽內容:
  6/12(三) 上課時間，會在R402進行模擬競賽，內容如下兩頁影片所示，先在Rviz中生成河內塔與障礙物，整合Lab4的IK程式讓手臂端末到達指定的位置與姿態，並抓起河內塔(變紫色)放到指定位置，重複直到堆疊完成。

## Slide 5: 2. Simulation Contest
影片1---無障礙物
https://www.youtube.com/watch?v=jG8LxCkJqKE

## Slide 6: 2. Simulation Contest
影片2---有障礙物
https://www.youtube.com/watch?v=x0SRCvkXIbY

## Slide 7: 2. Simulation Contest
競賽規則:
A
C
B
A
C
B
7 steps
規則1: (起始,最終)河內塔的位置，在各組出場前由助教隨機決定
規則2: 怕萬一實體競賽沒分數，有個備案，才舉行模擬競賽，不計分。必須加入障礙物，形狀可自由發揮。

## Slide 8: 2. Simulation Contest
Setup
  Download the mesh folder (from elearn) into /catkin_ws/src/myplan
  Download the 0_hanoi_planner.py and 0_hanoi_spawn_objects.py files into /myplan/src
Tutorial of how to spawn Hanoi towers in Rviz
  >>roslaunch myplan 0_demo.launch
  >>rosrun myplan 0_hanoi_spawn_objects.py

## Slide 9: 2. Simulation Contest
Flow Chart
9
MoveIt
path-planning
go_to_joint_state()
obstacle-avoidance
Spawn objects
add_box()
add_mesh()
Hanoi
your_code()
IK
Lab4_code()
Magnet on/off
attach_mesh()
detach_mesh()
a list of
(planned path)
Modify the sample code(/myplan/src/0_hanoi_planner.py)
You should add some parts of 0_hanoi_spawn_objects.py into 0_hanoi_planner.py.

## Slide 10: 2. Simulation Contest
Implementation:
  (1) >>roslaunch myplan 0_demo.launch
  (2) >>rosrun myplan 0_hanoi_planner.py

## Slide 11: 3. Real Arm Contest
競賽內容:
  6/19(三) 上課時間，會在R402舉行實體競賽，內容如下頁影片所示，並加上障礙物。各組手臂鎖在自己的木板上比賽，出場順序當場抽籤。

## Slide 12: 3. Real Arm Contest
Demo
https://youtu.be/qwChLCVZasA?si=9at6OJDTt-mp8WjW&t=5191

## Slide 13: 3. Real Arm Contest
Hardware Setup
  Connect electromagnet to driver board (ElecMag ).
  Stick two sheets of graph paper onto the wooden board.
  Secure the robot arm to the board.
  Secure the hanoi-base to the board.
  Manage the wires to ensure stability.
Robot
Arm

## Slide 14: 3. Real Arm Contest
Firmware Setup
  Download new “Robotics_ST” from elearn and paste into main.cpp
  Modify the parameters.
開啟電磁鐵功能
微調校正角度
J3_CALI
J1_CALI

## Slide 15: 3. Real Arm Contest
Firmware Setup
  Download 0_magnet_moveit_real_arm_interface.py into /myrobot_control/src
  Download 0_magnet _serial_with_ST.py into /myrobot_control/src
  Modify your_keyboard_control in Lab3 to confirm every part works well.
0_magnet_serial_with_ST.py
Original (Lab3):
Joint_angle.data = [pi/2, 0, -pi/2, 0]
New (Lab5):
Joint_angle.data = [pi/2, 0, -pi/2, 0, eef_state]
yourKeyboardControl.py
yourKeyboardControl.cpp
/real_robot_arm_joint
(Float64MultiArray)

## Slide 16: 3. Real Arm Contest
Flow Chart
0_magnet_moveit_real_
arm_interface.py
0_magnet_serial_with_ST.py
MoveIt
path-planning
go_to_joint_state()
obstacle-avoidance
Spawn objects
add_box()
add_mesh()
Hanoi
your_code()
IK
Lab4_code()
Magnet on/off
pub_EefState_to_arm()
a list of
(planned path)
Combine the sample code
(/myplan/src/0_hanoi_planner.py)
(/myplan/src/0_hanoi_spawn_objects.py)
/SetEndEffector
(Bool)

## Slide 17: 3. Real Arm Contest
Implementation :
  (1) Make sure the real robot in Home Position(as graph).
    Calibrate first (hold blue and click black)
  (2) >>roslaunch myplan 0_demo.launch
  (3) >> rosrun myrobot_control 0_magnet_moveit_real_arm_interface.py
  (4) >> rosrun myrobot_control 0_magnet_serial_with_ST.py
  (5) Set up power supply, 12V parallel 3A 3A
  (Keep a finger on the power button)
  (6) >>rosrun myplan 0_hanoi_planner.py
Home Position

## Slide 18: To be released…
模擬競賽詳細規則與細節(如: 時間表)
實體競賽詳細規則與細節(如: 晉級規定、障礙物形狀等)

## Slide 19: 舊競賽規則參考
競賽規則:
規則1: (起始,最終)河內塔的位置，會在各組出場前由助教抽籤決定
A
C
B
A
C
B
7 steps
這個範例中，起始河內塔在A位置，最終要搬到B位置，縮寫成(A,B)

## Slide 20: 舊競賽規則參考
競賽規則:
Mission Completed:
for each “successful stacking” 7 steps
(You can rescue the tower from falling down instantly,
but the 10 points will be taken off.)
規則2:計分方式
70
To goal within 45 secs, some extra works should be done.

## Slide 21: 舊競賽規則參考
競賽規則:
Leave the home position
(Time start)
(Time runs)
(Time stop)
Mission complete
and
go back to home position
Stack the towers
規則3:計時方式

## Slide 22: 舊競賽規則參考
競賽規則:
規則4: 若兩組分數相同，耗時較少者勝出。

## Slide 23: 舊賽程表參考
賽程表如下頁，以下為文字說明:
各組會被分到A(4組), B(3組), C(3組)進行第一輪競賽
ABC組內，積分最高者，直接晉級最後一輪
A組(第二三名)、BC組(第二名)進行四搶一復賽
ABC組內，積分最後者……淘汰QQ
最後一輪，從4組中取冠軍、亞軍、季軍

## Slide 24: 舊賽程表參考

## Slide 25: 4. Appendix
Some issues:
  由於TX2(CPU)算力較不足，且實驗河內塔的形狀不規則，在模擬環境做碰撞偵測、閉障、路徑規劃要算很久。若無法升級硬體，實體手臂競賽時，可以考慮把規畫好的路徑存取出來。
  Sample code內有河內塔幾何參數，若不清楚可直接到R402量測